## Slide 1: EINSTEIN TURTLEBOT Fall 2019
TODD TOWNSEND RUBEN MALDONADO TYSON FOSDICK NICHOLAS LONG

## Slide 2: Accomplishments
Resurrected to previous capabilities to establishing baseline.
Researched software improvements
Added Keyboard controls to control robot
Added to head and arm movements, more gestures, smoother movement – All working – debug needed in concurrency
Connected API’s and webhooks for vocal recognition
Improved speech synthesis, and increase library of vocabulary
Wrote script to perform in a theater play

## Slide 3: SPEECH SYNTHESIS
The following methods were used in speech synthesis.
Speech synthesis is accomplished using a text to speech web application – Google Cloud API
A script takes text phrases as input, leverages AWS polly speech synthesis tools that produce the mp3
Polly sends the file back for local playback

## Slide 4: VOCAL RECOGNITION
Vocal Recognition uses three distinct stages:
Recording-Einstein records audio using an onboard microphone and stores the files locally.
Voice Processing-Captured audio is sent to a Google speech to text API that returns processed audio as a string
In the response, the string is then compared to list of pre-selected responses, when a match is found, initiates appropriate gesture and sends text response to speech synthesis script.

## Slide 5: ROBOT THEATER ACTOR
We will control Einstein the Actor with one Director Host
Director node publishes desired gestures
One host will be used, keyboard control
Script controls for Acting Performances
Actor subscribes to Direct node and performs requested gestures
Would like to preform multiple actions concurrently
Director handles Voice synthesis and playback
Would like to extend to remote microphone direction

## Slide 6: CHALLENGES
The orientation of Einstein’s movements
Creating cross platform configurations
Troubleshooting servo wiring
Troubleshooting hardware configurations/availabilities
Determining the software for best functionality
Getting speech synthesis working with wifi capabilities
Coordinating speech synthesis with Robot movements
Exporting scripts into raspberry pi for Einsteins Acting performance

## Slide 7: Vision Processing
Using basic I/O Webcam with microphone
Basic Object Detection and Facial recognition
Image processing based on Obstacles
Facial recognition, keeps eye contact
Detects Obstacles and navigates accordingly

## Slide 8: FUTURE PLANS
Establish Einstein as the accomplished actor he should be
Create a stable launch file for ROS
Make arm and head movements based on facial recognition
Einstein raise arms and dance based on vision and commands
Einstein waive his arms and preforms based on commands
Have Einstein follow scripts for the robot theater
Have Einstein perform gestures based on user spoken intent input

## Slide 9: WHAT WE LEARNED
Hardware and Software setup takes a great deal of time to accomplish
Need to invest more time for debug after setup
Keep all configurations local and similar
The importance of Ros Workspace sourcing
Need to refine movements and gestures
Refine our skills with OpenCV, make movements and gestures funnier and based on the facial recognition system
Put more time into speech synthesis, need to make bridged connection for Internet